## Slide 1
JFK AIRPORT
Taxi-Out Time Analysis
What really drives delays between gate and takeoff?
Apostolos Karyofyllis · github.com/Karyapos

## Slide 2
THE PROBLEM
What is taxi-out time?
The time between a flight pushing back from the gate and wheels-up on the runway.
At a busy hub like JFK averaging 313 flights per day, peaking above 350 even a few extra minutes per aircraft compounds into significant costs across a full day of operations.
Fuel
Every idle minute burns jet fuel at the gate
Punctuality
Late departures cascade into missed connections
Emissions
Engines idling longer means more CO₂ per flight

## Slide 3
THE DATA & APPROACH
28,818
Flights analyzed
92
Days of data (2019–2020)
20.86
Avg. taxi-out time (min)
4-Phase Analysis Pipeline
01
SQL
Data cleaning & exploratory analysis
02
R
Correlation & statistical testing
03
Power BI
Interactive dashboard
04
ML
LASSO · GAM · Random Forest

## Slide 4
WHAT WE FOUND
Chart: Taxi-Out Time by Departure Traffic Level (min)
| Very Low | Low | Moderate | High | Very High
Avg Taxi-Out (min) | 17.7 | 19.03 | 20.58 | 22.04 | 22.78
Traffic is the #1 driver
More planes queuing = longer waits. “Very High” traffic averages 22.8 min vs 17.7 min at “Very Low” a 5-minute gap that multiplies across hundreds of daily flights.
Wind matters, but modestly
ENE wind shows a detectable effect, raising taxi-out average by 2.3 minutes. However, it occurs in only 3.9% of flights, making it a high-impact, low-frequency event.
Weather (mostly) doesn't explain it
Temperature, rain, pressure, humidity, almost no relationship with taxi-out times. The data said no.

## Slide 5
WHERE TO GO FROM HERE
Directions worth exploring
25%
of flights depart
in the 7–9 window
13%
depart in the
18–19 window alone
5 min
difference, Very Low
vs Very High traffic
3.9%
ENE wind frequency
highly predictable
01
Spread Departure Slots
The 7–9 and 18–19 windows concentrate too many departures. De-peaking schedules would reduce queue pressure and shorten taxi-out times across the board. The data strongly supports this direction.
High priority · Structural fix
02
Pre-Position Resources at Peak Times
Ground crew and ATC capacity during the 7–9 and 18–19 windows, and during ENE wind forecasts, could reduce bottlenecks before they form. ENE wind is rare but predictable, an early-warning protocol is feasible.
Operational · Near-term
03
Coordinate with Airlines on Slot Policy
Peak scheduling is airline-driven, not airport-driven. The real lever is coordination at the scheduling level. Worth investigating what peer airports have done with slot management.
Policy · Research needed

## Slide 6
Thanks for reading.
Full project end-to-end analysis:
github.com/Karyapos
SQL · EDA & Cleaning
R · Correlation & Modeling
Power BI · Dashboard
ML · Random Forest
Apostolos Karyofyllis